## Slide 1
Need for fast and accurate prediction of large phased array antennas pattern in front of a beamsteering process:
Finite elements (FE) with geometric multigrid preconditioned iterative solvers are employed for near field computations (including antennas coupling, dielectric losses, etc.)
Near field to far field transformation (N2F): Stratton-Chu formulas for pattern computation using a Fourier approximation (FFT)
A projection-based model order reduction (MOR) allows for significant pattern computations speedup
Fast phased array pattern computations

## Slide 2
Projection-based MOR: V is a collection of P linearly independent solutions for different scan angles (θs,ϕs)
Reduced order radiation system
Full radiation system
FE
N2F
Complex weighting at ports excitations
Radiation Model

## Slide 3
Rank(V) = 15 (n° of antennas)
n° of DoFs: 358' 648  15
Memory usage: 625 MB  1.5 MB
MOR error: ε ≤ 10-11
2D-DFT truncation error: εn2f ≤ 10-4
≈ 0.01 dB max. gain error
Whole movie:
for HFSS (commercial package) 10 h 20 min
for the full parameterized model: 1 min 3 s
for the reduced parameterized model: 8 s
Numerical results for 3x5 patch antennas array